## Slide 1: Trend Emisi Sektor Energi dan Transportasi IPB
IPB University
"Zero Waste, Zero Emission, Rich in Bio-and Cultural-diversity"

## Slide 2: Roadmap of LC Campus Scenario Modelling with Monitoring
Modeling
Current policy programs
Available data
Number of students and faculty & economy
Transport volume
Land-use change
Waste generation
Energy demand
Emission reduction
Energy demand
Preliminary
Scenario
Monitoring & analysis
Modeling
Energy consumption pattern in IPB Campus
Energy consumption
Awareness on energy and environment
Transportation behavior
Energy saving potential of buildings in IPB Campus
Updated
Scenario
Projection with monitoring data
GHG emission reduction potential considering local characteristics in IPB Campus
Actions and Candidates
of Policy Programs
We have developed model and LCS scenarios in IPB with available data and current policy initiatives.
The scenario will be updated with ongoing monitoring data and survey results
Sep-Dec 2018
Dec 2018-Jan 2019
Questionnaire survey
Data pembayaran listrik
Inventarisasi peralatan listrik

## Slide 3: Energy Monitoring
2014, CCROM-IPB supported with NIES, start to study the behavior of Bogor city and IPB Campus energy consumption
  Base line data for the future energy policy
Electricity consumption in many points of offices, commercials, houses of Bogor city and IPB campus have been monitored:
  System provided by Fujitsu and Fuji electric
Limitation
  At Dramaga campus, the monitoring system in only installed at the Rectorate Office
  Additional energy monitoring system for Darmaga Campus is designed by IPB to complement the Fujitsu and Fuji Electric

## Slide 4
Weekly Monitoring Data in Bogor City
Sun
2/28
Mon
2/29
Tue
3/1
Wed
3/2
Thu
3/3
Fri
3/4
Sat
3/5
Sun
2/28
Mon
2/29
Tue
3/1
Wed
3/2
Thu
3/3
Fri
3/4
Sat
3/5
Sun
2/28
Mon
2/29
Tue
3/1
Wed
3/2
Thu
3/3
Fri
3/4
Sat
3/5
Sun
2/28
Mon
2/29
Tue
3/1
Wed
3/2
Thu
3/3
Fri
3/4
Sat
3/5
Sun
2/28
Mon
2/29
Tue
3/1
Wed
3/2
Thu
3/3
Fri
3/4
Sat
3/5
Office
Hotel
Cafe
Government
House
hold
AC
Lighting
Receptacle
Electricity consumption by air-conditioners is high in all monitored sites
Refrigerator
4

## Slide 5: Monitoring of Electricity Consumption for designing strategy for reducing emission
Identify target area
Monitor energy use
Processed and analyze the data
Identify main sources of energy consumption
Evaluate impact of the scenarios
Design scenarios
Select scenario

## Slide 6: Measures to reduce emissions from electricity consumption at IPB Campus
Identify target area
Monitor energy use
Processed and analyze the data
Identify main source of energy consumption
Evaluate impact of the scenarios
Design scenarios
Select scenario
Campus facilities that consume most of campus electricity need to be studied (monitored)

## Slide 7: Energy Monitoring at Rectorate IPB
Identify target area
Monitor energy use
Processed and analyze the data
Identify main source of energy consumption
Evaluate impact of the scenarios
Design scenarios
Select scenario

## Slide 8: Energy Monitoring at Rectorate IPB
There is a significance increase on the use of energy at Rectorate at 6 am to 8 pm, mainly due to the increase use of energy for air conditioning
Identify target area
Monitor energy use
Processed and analyze the data
Identify main source of energy consumption
Evaluate impact of the scenarios
Design scenarios
Select scenario

## Slide 9: Measures to reduce emissions from electricity consumption at IPB Campus
Main source of energy consumption is Air conditioning
Identify target area
Monitor energy use
Processed and analyze the data
Identify main source of energy consumption
Evaluate impact of the scenarios
Design scenarios
Select scenario
Main source of energy consumption

## Slide 10: Measures to reduce emissions from electricity consumption at IPB Campus
Identify target area
Monitor energy use
Processed and analyze the data
Identify main source of energy consumption
Evaluate impact of the scenarios
Design scenarios
Select scenario
Scenarios
Technology options
Replacement of lights that will improved efficiency of 70%
Replacement of air conditioning that will improve efficiency of 17%
Scenario name | Lighting | Air conditioning
BAU |  | 
S1 | 100% replacement | None
S2 | None | 100% replacement
S3 | 50% replacement | 50% replacement

## Slide 11: Measures to reduce emissions from electricity consumption at IPB Campus
Identify target area
Monitor energy use
Processed and analyze the data
Identify main source of energy consumption
Evaluate impact of the scenarios
Design scenarios
Select scenario
Scenarios
Behavior measures
Policy for limiting use of AC during peak hours (5-10 pm)
Policy for limiting use of certain appliance during off-peak hours
Scenario name | Peak hour | Off Peak hours
S4 | 25% reduction | None
S5 | None | No air conditioning between 8 pm – 6 am
S6 | 10% reduction | No air conditioning between 10 pm – 5 am
S7 | 10% reduction | 10% reduction

## Slide 12: Measures to reduce emissions from electricity consumption at IPB Campus
Chart: Electricity consumption (kwh/month)
| BAU | S1 | S2 | S3 | S4 | S5 | S6 | S7
Rektorat | 7074270 | 6523365.36 | 4255060.792 | 5802689.608 | 6818359.95 | 3677632.4 | 3587887.71 | 6366843
Technology option
Behavioral measures
In general, Scenario 4 resulted in lower reduction compare to other scenarios
Scenario 2 generates lower consumption, in Technology option but, scenario 6 is the best scenario generates low consumption
Identify target area
Monitor energy use
Processed and analyze the data
Identify main source of energy consumption
Evaluate impact of the scenarios
Design scenarios
Select scenario
Evaluating Impact

## Slide 13: Measures to reduce emissions from electricity consumption at IPB Campus
Chart: Emission (kgCO2/month)
| Base Year | Target
BaU | 5963609.61 | 5963609.61
S1 | 5963609.61 | 5499196.9985
S2 | 5963609.61 | 3587016.2477
S3 | 5963609.61 | 4891667.3395
S4 | 5963609.61 | 5747877.4379
S5 | 5963609.61 | 3100244.1132
S6 | 5963609.61 | 3024589.3395
S7 | 5963609.61 | 5367248.649
Identify target area
Monitor energy use
Processed and analyze the data
Identify main source of energy consumption
Evaluate impact of the scenarios
Design scenarios
Select scenario
Evaluating Impact

## Slide 14: Recapitulation of cost for electricity at IPB in 2019
NAMA PELANGGAN | ID PELANGGAN | Bulan | Tot. KWh | Σ bayar | Emisi | Emisi Skenario | 
 |  |  |  |  |  | S4 (low) | S6 (high)
Gedung FAK KAN NAK | 538311645719 | Jan-19 | 618,978 | 684,130,404 | 521,798 | 502,923 | 255,069
 |  | Feb-19 | 126,700 | 688,463,590 | 106,808 | 102,944 | 52,211
 |  | Mar-19 | 52,991 | 672,479,647 | 44,671 | 43,055 | 21,837
 |  | Apr-19 | 565,503 | 719,868,921 | 476,719 | 459,474 | 233,033
 |  | May-19 | 564,678 | 714,125,003 | 476,024 | 458,804 | 232,693
Based on the electricity cost of 2019, if the scenario S4 (low scenario) and S6 (high scenario) were used, the emission reduction will be 11,764 and 166,235 kgCO2/month respectively.
Data with yellow highlight need evaluation

## Slide 15: Measures to reduce emissions from electricity consumption at IPB Campus
Identify target area
Monitor energy use
Processed and analyze the data
Identify main source of energy consumption
Evaluate impact of the scenarios
Design scenarios
Select scenario
Selection of Scenarios
Consideration can be based on, among others:
Least cost (total)
Highest emission reduction
Highest emission reduction/cost, especially for technology based

## Slide 16: Transportation

## Slide 17: Ritase
Chart: 
| 42917 | 42948 | 42979 | 43009 | 43040 | 43070
Bau | 2764.6465 | 3254.3336 | 4424.7519 | 6043.1351 | 5426.0853 | 4345.6992
Green Campus | 2398.9669 | 2823.8832 | 3839.4904 | 5243.8102 | 4866.3401 | 3885.1929
Chart: 
| Jul | Aug | Sep | Oct | Nov | Dec
Bus | 1259 | 1482 | 2015 | 2752 | 2471 | 1979
Moli | 5271 | 3814
Rata-rata perhari
Bus 22; Moli 12
Assumption of BaU developed based on survey
Bus 40%
Car 20%
Motor cycle 40%
Green transportation policy (Bus and Moli)
Reduce the use motor cycle in campus with increasing bus system
Reduce the use of BBM due to the use of Moli

## Slide 18: Ritase
Chart: 
| Jul | Aug | Sep | Oct | Nov | Dec
Bus | 1259 | 1482 | 2015 | 2752 | 2471 | 1979
Moli | 5271 | 3814
Rata-rata per hari
Bus 22; Mobil listrik (Moli) 12
533 kg CO2/month